## Slide 1: Project Course Drives Systems and Power Electronics
Study on Dual Active Bridge Converter
Participants
Sandip Guha Thakurta
Rituraj Mukherjee
Chintu Seth
Supervisor
Qifan Yang
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich

## Slide 2
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich
Standard topology of a DAB converter
8 power switches forming the two bridges
1 HF transformer to provide isolation and voltage level matching
1 energy-storing inductor – series combination of leakage inductances and any additional inductance connected to the primary

## Slide 3
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich
Advantages
Isolated bidirectional converter (IBDC) – galvanic isolation between input and output and bidirectional power flow
High Power capabilities compared to other IBDCs because of the 8 active switches.
Possibilities of soft switching.
High efficiency and Power density
Smaller size of passive components

## Slide 4
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich
Standard modulation techniques
The power flow is controlled by the current flowing through the inductor, or the primary and secondary voltages.
Voltages are controlled by the corresponding duty cycle and phase angle
Single Phase Shift Modulation (SPS): The duty cycle of primary and secondary bridge is kept constant at 50%. Power flow is controlled by the phase difference between the two voltages.
Dual Phase Shift Modulation (DPS): Apart from the phase shift between the input and output H bridges, there is an inner phase shift between the legs of individual H bridges.
Extended Phase Shift Modulation (EPS): The inner phase shift is applied to either the input H bridge or the output H bridge.
Triple Phase shift Modulation (TPS): The inner phase shift is different for the individual bridges.

## Slide 5
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich
Applications
EV charger
Solid-state transformer
Modular multilevel dc-link solid-state transformer
Aerospace applications

## Slide 6
Chair of High Power Converter Systems
TUM School of Engineering and Design
Technical University of Munich
Possible research works
Hardware/Circuit optimization: Non-resonant DAB is widely used, some resonant DAB topologies can be investigated for extending ZVS/ZCS range.
Control optimization:
Proper choice of modulation scheme
Efficiency optimization
Dynamic performance optimization